Lab 6 – Anirudh Sriram

Tasks

  1. Adding SLT - I modified the ALU and ALU control logic to set output equal to 1 if a was less than b. This was done using beahvioural Verilog.

  2. Adding ADDI - I created a seperate block in the control file, which runs ADDI, based on the initial instruction. I linked this to the ALU, to perform the add instruction.

  3. Adding Jump Instruction - Created a new instance of the mux, which takes in as the input the first four bits as the PC + 4, and the next 28 bits from the Jump address. This is fed back into the program counter.

  4. Adding BNE Instruction - I added extra logic for this instruction. There were 2 AND gates, a NOT gate and an OR Gate, as well as the new Instruction in the Control file. The logic design can be seen in the attached diagram.

  5. Adding LUI Instruction - For this instruction I added again a new instruction in the Control file. The immediate value loaded in the instruction was shifted left sixteen bits and added to the given register.